## Slide 1: Chapter 1 Digital Systems and Binary Numbers
Digital Logic Design

## Slide 2: Outline of Chapter 1
1.1 Digital Systems
1.2 Binary Numbers
1.3 Number-base Conversions
1.4 Octal and Hexadecimal Numbers
1.5 Complements
1.6 Signed Binary Numbers
1.7 Binary Codes
1.8 Binary Storage and Registers
1.9 Binary Logic

## Slide 3: Digital Systems and Binary Numbers
Digital age and information age
Digital computers
  General purposes
  Many scientific, industrial and commercial applications
Digital systems
  Telephone switching exchanges
  Digital camera
  Electronic calculators, PDA's
  Digital TV
Discrete information-processing systems
  Manipulate discrete elements of information
  For example, {1, 2, 3, …} and {A, B, C, …}…

## Slide 4: Analog and Digital Signal
Analog system
  The physical quantities or signals may vary continuously over a specified range.
Digital system
  The physical quantities or signals can assume only discrete values.
  Greater accuracy
t
X(t)
t
X(t)
Analog signal
Digital signal

## Slide 5: Binary Digital Signal
An information variable represented by physical quantity.
For digital systems, the variable takes on discrete values.
  Two level, or binary values are the most prevalent values.
Binary values are represented abstractly by:
  Digits 0 and 1
  Words (symbols) False (F) and True (T)
  Words (symbols) Low (L) and High (H)
  And words On and Off
Binary values are represented by values or ranges of values of physical quantities.
t
V(t)
Binary digital signal
Logic 1
Logic 0
undefine

## Slide 6: Decimal Number System
Base (also called radix) = 10
  10 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Digit Position
  Integer & fraction
Digit Weight
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
5
1
2
7
4
10
1
0.1
100
0.01
500
10
2
0.7
0.04
d2*B2+d1*B1+d0*B0+d-1*B-1+d-2*B-2
(512.74)10

## Slide 7: Octal Number System
Base = 8
  8 digits { 0, 1, 2, 3, 4, 5, 6, 7 }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
8
1
1/8
64
1/64
5
1
2
7
4
5 *82+1 *81+2 *80+7 *8-1+4 *8-2
=(330.9375)10
(512.74)8

## Slide 8: Binary Number System
Base = 2
  2 digits { 0, 1 }, called binary digits or “bits”
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Bit x Weight”
Formal Notation
Groups of bits 4 bits = Nibble
8 bits = Byte
1
0
-1
2
-2
2
1
1/2
4
1/4
1
0
1
0
1
1 *22+0 *21+1 *20+0 *2-1+1 *2-2
=(5.25)10
(101.01)2
1 0 1 1
1 1 0 0 0 1 0 1

## Slide 9: Hexadecimal Number System
Base = 16
  16 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
16
1
1/16
256
1/256
1
E
5
7
A
1 *162+14 *161+5 *160+7 *16-1+10 *16-2
=(485.4765625)10
(1E5.7A)16

## Slide 10: The Power of 2
n | 2n
0 | 20=1
1 | 21=2
2 | 22=4
3 | 23=8
4 | 24=16
5 | 25=32
6 | 26=64
7 | 27=128
n | 2n
8 | 28=256
9 | 29=512
10 | 210=1024
11 | 211=2048
12 | 212=4096
20 | 220=1M
30 | 230=1G
40 | 240=1T
Mega
Giga
Tera
Kilo

## Slide 11: Addition
Decimal Addition
5
5
5
5
+
0
1
1
= Ten ≥ Base
 Subtract a Base
1
1
Carry

## Slide 12: Binary Addition
Column Addition
1
0
1
1
1
1
1
1
1
1
0
+
0
0
0
0
1
1
1
≥ (2)10
1
1
1
1
1
1
= 61
= 23
= 84

## Slide 13: Binary Subtraction
Borrow a “Base” when needed
0
0
1
1
1
0
1
1
1
1
0
−
0
1
0
1
1
1
0
= (10)2
2
2
2
2
1
0
0
0
1
= 77
= 23
= 54

## Slide 14: Binary Multiplication
Bit by bit
0
1
1
1
1
0
1
1
0
0
0
0
0
0
0
1
1
1
1
0
1
1
1
1
0
0
0
0
0
0
1
1
0
1
1
1
0
x

## Slide 15: Number Base Conversions
Decimal
(Base 10)
Octal
(Base 8)
Binary
(Base 2)
Hexadecimal
(Base 16)
Evaluate Magnitude
Evaluate Magnitude
Evaluate Magnitude

## Slide 16: Decimal (Integer) to Binary Conversion
Divide the number by the ‘Base’ (=2)
Take the remainder (either 0 or 1) as a coefficient
Take the quotient and repeat the division
Example: (13)10
Quotient
Remainder
Coefficient
Answer: (13)10 = (a3 a2 a1 a0)2 = (1101)2
MSB LSB
13
/ 2 = 6
1 a0 = 1
6
/ 2 = 3
0 a1 = 0
3
/ 2 = 1
1 a2 = 1
1
/ 2 = 0
1 a3 = 1

## Slide 17: Decimal (Fraction) to Binary Conversion
Multiply the number by the ‘Base’ (=2)
Take the integer (either 0 or 1) as a coefficient
Take the resultant fraction and repeat the division
Example: (0.625)10
Integer
Fraction
Coefficient
Answer: (0.625)10 = (0.a-1 a-2 a-3)2 = (0.101)2
MSB LSB
0.625
* 2 = 1 . 25
0.25
* 2 = 0 . 5 a-2 = 0
0.5
* 2 = 1 . 0 a-3 = 1
a-1 = 1

## Slide 18: Decimal to Octal Conversion
Example: (175)10
Quotient
Remainder
Coefficient
Answer: (175)10 = (a2 a1 a0)8 = (257)8
175
/ 8 = 21
7 a0 = 7
21
/ 8 = 2
5 a1 = 5
2
/ 8 = 0
2 a2 = 2
Example: (0.3125)10
Integer
Fraction
Coefficient
Answer: (0.3125)10 = (0.a-1 a-2 a-3)8 = (0.24)8
0.3125
* 8 = 2 . 5
0.5
* 8 = 4 . 0 a-2 = 4
a-1 = 2

## Slide 19: Binary − Octal Conversion
8 = 23
Each group of 3 bits represents an octal digit
Octal | Binary
0 | 0 0 0
1 | 0 0 1
2 | 0 1 0
3 | 0 1 1
4 | 1 0 0
5 | 1 0 1
6 | 1 1 0
7 | 1 1 1
Example:
( 1 0 1 1 0 . 0 1 )2
( 2 6 . 2 )8
Assume Zeros
Works both ways (Binary to Octal & Octal to Binary)

## Slide 20: Binary − Hexadecimal Conversion
16 = 24
Each group of 4 bits represents a hexadecimal digit
Hex | Binary
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
A | 1 0 1 0
B | 1 0 1 1
C | 1 1 0 0
D | 1 1 0 1
E | 1 1 1 0
F | 1 1 1 1
Example:
( 1 0 1 1 0 . 0 1 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Binary to Hex & Hex to Binary)

## Slide 21: Octal − Hexadecimal Conversion
Convert to Binary as an intermediate step
Example:
( 0 1 0 1 1 0 . 0 1 0 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Octal to Hex & Hex to Octal)
( 2 6 . 2 )8
Assume Zeros

## Slide 22: Decimal, Binary, Octal and Hexadecimal
Decimal | Binary | Octal | Hex
00 | 0000 | 00 | 0
01 | 0001 | 01 | 1
02 | 0010 | 02 | 2
03 | 0011 | 03 | 3
04 | 0100 | 04 | 4
05 | 0101 | 05 | 5
06 | 0110 | 06 | 6
07 | 0111 | 07 | 7
08 | 1000 | 10 | 8
09 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 23: 1.5 Complements
There are two types of complements for each base-r system: the radix complement and diminished radix complement.
Diminished Radix Complement - (r-1)’s Complement
  Given a number N in base r having n digits, the (r–1)’s complement of N is defined as:
  (rn –1) – N
Example for 6-digit decimal numbers:
  9’s complement is (rn – 1)–N = (106–1)–N = 999999–N
  9’s complement of 546700 is 999999–546700 = 453299
Example for 7-digit binary numbers:
  1’s complement is (rn – 1) – N = (27–1)–N = 1111111–N
  1’s complement of 1011000 is 1111111–1011000 = 0100111
Observation:
  Subtraction from (rn – 1) will never require a borrow
  Diminished radix complement can be computed digit-by-digit
  For binary: 1 – 0 = 1 and 1 – 1 = 0

## Slide 24: Complements
1’s Complement (Diminished Radix Complement)
  All ‘0’s become ‘1’s
  All ‘1’s become ‘0’s
  Example (10110000)2
   (01001111)2
  If you add a number and its 1’s complement …
1 0 1 1 0 0 0 0
+ 0 1 0 0 1 1 1 1
1 1 1 1 1 1 1 1

## Slide 25: Complements
Radix Complement
Example: Base-10
Example: Base-2
The r's complement of an n-digit number N in base r is defined as
rn – N for N ≠ 0 and as 0 for N = 0. Comparing with the (r  1) 's complement, we note that the r's complement is obtained by adding 1 to the (r  1) 's complement, since rn – N = [(rn  1) – N] + 1.
The 10's complement of 012398 is 987602
The 10's complement of 246700 is 753300
The 2's complement of 1101100 is 0010100
The 2's complement of 0110111 is 1001001

## Slide 26: Complements
2’s Complement (Radix Complement)
  Take 1’s complement then add 1
  Toggle all bits to the left of the first ‘1’ from the right
  Example:
  Number:
  1’s Comp.:
0 1 0 1 0 0 0 0
1 0 1 1 0 0 0 0
0 1 0 0 1 1 1 1
+ 1
OR
1 0 1 1 0 0 0 0
0
0
0
0
1
0
1
0

## Slide 27: Complements
Subtraction with Complements
  The subtraction of two n-digit unsigned numbers M – N in base r can be done as follows:

## Slide 28: Complements
Example 1.5
  Using 10's complement, subtract 72532 – 3250.
Example 1.6
  Using 10's complement, subtract 3250 – 72532.
There is no end carry.
Therefore, the answer is – (10's complement of 30718) =  69282.

## Slide 29: Complements
Example 1.7
  Given the two binary numbers X = 1010100 and Y = 1000011, perform the subtraction (a) X – Y ; and (b) Y  X, by using 2's complement.
There is no end carry. Therefore, the answer is Y – X =  (2's complement of 1101111) =  0010001.

## Slide 30: Complements
Subtraction of unsigned numbers can also be done by means of the (r  1)'s complement. Remember that the (r  1) 's complement is one less then the r's complement.
Example 1.8
  Repeat Example 1.7, but this time using 1's complement.
There is no end carry, Therefore, the answer is Y – X =  (1's complement of 1101110) =  0010001.

## Slide 31: 1.6 Signed Binary Numbers
To represent negative integers, we need a notation for negative values.
It is customary to represent the sign with a bit placed in the leftmost position of the number since binary digits.
The convention is to make the sign bit 0 for positive and 1 for negative.
Example:
Table 1.3 lists all possible four-bit signed binary numbers in the three representations.

## Slide 32: Signed Binary Numbers

## Slide 33: Signed Binary Numbers
Arithmetic addition
  The addition of two numbers in the signed-magnitude system follows the rules of ordinary arithmetic. If the signs are the same, we add the two magnitudes and give the sum the common sign. If the signs are different, we subtract the smaller magnitude from the larger and give the difference the sign if the larger magnitude.
  The addition of two signed binary numbers with negative numbers represented in signed-2's-complement form is obtained from the addition of the two numbers, including their sign bits.
  A carry out of the sign-bit position is discarded.
Example:

## Slide 34: Signed Binary Numbers
Arithmetic Subtraction
  In 2’s-complement form:
Example:
Take the 2’s complement of the subtrahend (including the sign bit) and add it to the minuend (including sign bit).
A carry out of sign-bit position is discarded.
( 6)  ( 13)
(11111010  11110011)
(11111010 + 00001101)
00000111 (+ 7)

## Slide 35: 1.7 Binary Codes
BCD Code
  A number with k decimal digits will require 4k bits in BCD.
  Decimal 396 is represented in BCD with 12bits as 0011 1001 0110, with each group of 4 bits representing one decimal digit.
  A decimal number in BCD is the same as its equivalent binary number only when the number is between 0 and 9.
  The binary combinations 1010 through 1111 are not used and have no meaning in BCD.

## Slide 36: Binary Code
Example:
  Consider decimal 185 and its corresponding value in BCD and binary:
BCD addition

## Slide 37: Binary Code
Example:
  Consider the addition of 184 + 576 = 760 in BCD:
Decimal Arithmetic: (+375) + (-240) = +135
Hint 6: using 10’s of BCD

## Slide 38: Binary Codes
Other Decimal Codes

## Slide 39: Binary Codes)
Gray Code
  The advantage is that only bit in the code group changes in going from one number to the next.
    Error detection.
    Representation of analog data.
    Low power design.
000
001
010
100
110
111
101
011
1-1 and onto!!

## Slide 40: Binary Codes
American Standard Code for Information Interchange (ASCII) Character Code

## Slide 41: Binary Codes
ASCII Character Code

## Slide 42: ASCII Character Codes
American Standard Code for Information Interchange (Refer to Table 1.7)
A popular code used to represent information sent as character-based data.
It uses 7-bits to represent:
  94 Graphic printing characters.
  34 Non-printing characters.
Some non-printing characters are used for text format (e.g. BS = Backspace, CR = carriage return).
Other non-printing characters are used for record marking and flow control (e.g. STX and ETX start and end text areas).

## Slide 43: ASCII Properties
ASCII has some interesting properties:
  Digits 0 to 9 span Hexadecimal values 3016 to 3916
  Upper case A-Z span 4116 to 5A16
  Lower case a-z span 6116 to 7A16
    Lower to upper case translation (and vice versa) occurs by flipping bit 6.

## Slide 44: Binary Codes
Error-Detecting Code
  To detect errors in data communication and processing, an eighth bit is sometimes added to the ASCII character to indicate its parity.
  A parity bit is an extra bit included with a message to make the total number of 1's either even or odd.
Example:
  Consider the following two characters and their even and odd parity:

## Slide 45: Binary Codes
Error-Detecting Code
  Redundancy (e.g. extra information), in the form of extra bits, can be incorporated into binary code words to detect and correct errors.
  A simple form of redundancy is parity, an extra bit appended onto the code word to make the number of 1’s odd or even. Parity can detect all single-bit errors and some multiple-bit errors.
  A code word has even parity if the number of 1’s in the code word is even.
  A code word has odd parity if the number of 1’s in the code word is odd.
  Example:
10001001
10001001
1
0
(odd parity)
Message B:
Message A:
(even parity)

## Slide 46: 1.8 Binary Storage and Registers
Registers
  A binary cell is a device that possesses two stable states and is capable of storing one of the two states.
  A register is a group of binary cells. A register with n cells can store any discrete quantity of information that contains n bits.
A binary cell
  Two stable state
  Store one bit of information
  Examples: flip-flop circuits, ferrite cores, capacitor
A register
  A group of binary cells
  AX in x86 CPU
Register Transfer
  A transfer of the information stored in one register to another.
  One of the major operations in digital system.
  An example in next slides.
n cells
2n possible states

## Slide 47: A Digital Computer Example
Synchronous or Asynchronous?
Inputs: Keyboard, mouse, modem, microphone
Outputs: CRT, LCD, modem, speakers

## Slide 48: Transfer of information
Figure 1.1 Transfer of information among register

## Slide 49: Transfer of information
The other major component of a digital system
  Circuit elements to manipulate individual bits of information
  Load-store machine
    LD R1;
    LD R2;
    ADD R3, R2, R1;
    SD R3;
Figure 1.2 Example of binary information processing

## Slide 50: 1.9 Binary Logic
Definition of Binary Logic
  Binary logic consists of binary variables and a set of logical operations.
  The variables are designated by letters of the alphabet, such as A, B, C, x, y, z, etc, with each variable having two and only two distinct possible values: 1 and 0,
  Three basic logical operations: AND, OR, and NOT.

## Slide 51: Binary Logic
Truth Tables, Boolean Expressions, and Logic Gates
x | y | z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | z
0 | 1
1 | 0
AND
OR
NOT
z = x • y = x y
z = x + y
z = x = x’

## Slide 52: Switching Circuits
AND
OR

## Slide 53: Binary Logic
Logic gates
  Example of binary signals
0
1
2
3
Logic 1
Logic 0
Un-define
Figure 1.3 Example of binary signals

## Slide 54: Binary Logic
Logic gates
  Graphic Symbols and Input-Output Signals for Logic gates:
Fig. 1.4 Symbols for digital logic circuits
Fig. 1.5 Input-Output signals for gates

## Slide 55: Binary Logic
Logic gates
  Graphic Symbols and Input-Output Signals for Logic gates:
Fig. 1.6 Gates with multiple inputs